## Slide 1: Brute-force Algorithm Outline
For each cell element
  Calculate its distance from each of the solid faces
  Wall distance is the minimum of these distances
Face centers
Cell centers
Wall distance for this cell = minimum distance from faces

## Slide 2: Brute-force – Serial

## Slide 3: Brute-force – Parallel (Block Per Cell)
Each block calculates wall distance for a cell
  Each thread calculates distance from a face
  Reduce minimum to get wall distance
Face centers
Cell centers
Calculated by a thread
Reduce min per block to get wall distance for this cell

## Slide 4: Brute-force – Parallel (Block Per Cell)
Implemented 3 variations
  (A): Shared memory writes for face distances
  (B): (A) + Shared memory reads to face (x, y) arrays
  (C): Same as (B) with (x, y) arrays converted to an interspersed array for coalesced shared mem reads
  i.e. x0, y0, x1, y1, ....

## Slide 5: Brute-force – Parallel (Thread Per Cell)
Each thread calculates wall distance for a cell
  Calculates distance from the cell to each of the faces
  Keeps “running” min distance value as each faces distance gets calculated
Face centers
Cell centers
Loop within a thread calculates the distance
Running min distance per thread to get wall distance for this cell

## Slide 6: Brute-force – Parallel (Thread Per Cell)
Implemented 3 variations
  (A): Each thread calculates wall distance for a cell
  (B): Shared memory reads to face (x, y) arrays
  (C): Same as (A) with (x, y) arrays converted to an interspersed array for coalesced global mem reads
  i.e. x0, y0, x1, y1, ....

## Slide 7: Brute-force – Verification
Output from serial algorithm visually inspected for correctness
Outputs from parallel algorithms verified by comparing against serial algorithm output

## Slide 8: Brute-force – Performance
Algorithm | Small Grid (msec) | Fine Grid (msec) | Extra Fine Grid (msec)
Serial | 33 | 595 | 13636
Block Per Cell (1A) - Shared mem writes | 1 | 28 | -
Block Per Cell (1B) - Shared mem reads | 1 | 30 | -
Block Per Cell (1C) - Coalesced shared mem reads | 1 | 31 | -
Thread Per Cell (2A) | <1 | 7 | 173
Thread Per Cell (2B) - Shared mem reads | 1 | 9 | 293
Thread Per Cell (2C) - Coalesced global mem reads | <1 | 7 | 166
82x speedup vs. serial