## Slide 1: GPU acceleration of wall distance calculation for computational fluid dynamics codes
Nathan Wukie Vasanth Ganapathy Chris Park

## Slide 2: Outline
Background
Brute-force algorithm
Advancing boundary algorithm

## Slide 3: Background
Reynolds-Averaged Navier-Stokes calculation
Conservation of mass
Conservation of momentum
Conservation of energy
Wukie et al. 2012

## Slide 4: Background
Turbulence modeling
Conservation of mass
Conservation of momentum
Conservation of energy
Wukie et al. 2012

## Slide 5: Background
Cell-centered, Finite Volume discretization
Solution variables stored at cell-center

## Slide 6: Background
Moving mesh calculation

## Slide 7: Background
Test case: circle
Computational grid
Wall distance field

## Slide 8: Brute-force algorithm

## Slide 9: Brute-force Algorithm Outline
For each cell element
  Calculate its distance from each of the solid faces
  Wall distance is the minimum of these distances
Face centers
Cell centers
Wall distance for this cell = minimum distance from faces

## Slide 10: Brute-force – Serial

## Slide 11: Brute-force – Parallel (Block Per Cell)
Each block calculates wall distance for a cell
  Each thread calculates distance from a face
  Reduce minimum to get wall distance
Face centers
Cell centers
Calculated by a thread
Reduce min per block to get wall distance for this cell

## Slide 12: Brute-force – Parallel (Block Per Cell)
Implemented 3 variations
  (A): Shared memory writes for face distances
  (B): (A) + Shared memory reads to face (x, y) arrays
  (C): Same as (B) with (x, y) arrays converted to an interspersed array for coalesced shared mem reads
  i.e. x0, y0, x1, y1, ....

## Slide 13: Brute-force – Parallel (Thread Per Cell)
Each thread calculates wall distance for a cell
  Calculates distance from the cell to each of the faces
  Keeps “running” min distance value as each faces distance gets calculated
Face centers
Cell centers
Loop within a thread calculates the distance
Running min distance per thread to get wall distance for this cell

## Slide 14: Brute-force – Parallel (Thread Per Cell)
Implemented 3 variations
  (A): Each thread calculates wall distance for a cell
  (B): Shared memory reads to face (x, y) arrays
  (C): Same as (A) with (x, y) arrays converted to an interspersed array for coalesced global mem reads
  i.e. x0, y0, x1, y1, ....

## Slide 15: Brute-force – Verification
Output from serial algorithm visually inspected for correctness
Outputs from parallel algorithms verified by comparing against serial algorithm output

## Slide 16: Brute-force – Performance
Algorithm | Small Grid (msec) | Fine Grid (msec) | Extra Fine Grid (msec)
Serial | 33 | 595 | 13636
Block Per Cell (1A) - Shared mem writes | 1 | 28 | -
Block Per Cell (1B) - Shared mem reads | 1 | 30 | -
Block Per Cell (1C) - Coalesced shared mem reads | 1 | 31 | -
Thread Per Cell (2A) | <1 | 7 | 173
Thread Per Cell (2B) - Shared mem reads | 1 | 9 | 293
Thread Per Cell (2C) - Coalesced global mem reads | <1 | 7 | 166
82x speedup vs. serial

## Slide 17: Advancing boundary algorithm

## Slide 18: Advancing Boundary Algorithm
Background: Pre-processor
Goal: create a smaller subset of faces that need searched

## Slide 19: Advancing Boundary Algorithm
Background: Pre-processor
Goal: create a smaller subset of faces that need searched

## Slide 20: Advancing Boundary Algorithm
Background: GPU-Kernel

## Slide 21: Advancing Boundary Algorithm
Background: GPU-Kernel
Original
Condensed

## Slide 22: Advancing Boundary Algorithm
Background: GPU-Kernel

## Slide 23: Advancing Boundary Algorithm
Implementation: Pre-processing

## Slide 25: Advancing Boundary Algorithm
Implementation: Aux Cells

## Slide 26: Advancing Boundary Algorithm

## Slide 27: Thank you…